## Slide 1: NR-MIMO in ‘Study on NR-PHY’
3GPP TR 38.802 V1.0.0 (2016-11)

## Slide 2
For NR, DL CSI measurement with X antenna ports is supported. At least for CSI acquisition, NR supports CSI-RS and SRS. [Editor's note] The value of X is under investigation, as
Study the values of X = 1, 2 ,4,8,12,16,20,24,28,32
CSI-RS configuration for NR also includes at least ‘number of antenna ports’. Configuration can be explicit or implicit. The number of CSI-RS antenna ports can be independently configured for periodic/semi-persistent CSI reporting and aperiodic CSI reporting
CSI-RS mapped in one or multiple [consecutive] symbols

## Slide 3
NR supports aperiodic transmission of CSI-RS. For CSI-RS transmission, in addition, NR supports at least one of following:
  Semi-persistent transmission
  Preconfigured CSI-RS resources can be activated or de-activated
  Periodic transmission (can be configured by higher layer signaling)
#87 Agreements:
NR supports semi-persistent CSI-RS transmissions
  Activation(s)/de-activation(s) of CSI-RS resource is triggered dynamically
    Note: “dynamically” here can be DCI and/or MAC CE based. FFS details.
NR supports semi-statically configured/re-configured periodic CSI-RS transmissions
FFS: Details on signaling mechanisms

## Slide 4
The following configurations of NR CSI-RS are supported.
UE-specific configuration to support
  Wideband CSI-RS, i.e. from UE perspective, the full bandwidth the UE is configured to operate with
  Partial-band CSI-RS, i.e. from UE perspective, part of the bandwidth the UE is configured to operate with

## Slide 5
NR supports aperiodic CSI reporting. NR also supports at least one of following:
Periodic CSI reporting
  It can be configured by higher layer
Semi-persistent CSI reporting
  Configuration of CSI reporting can be activated or de-activated
#87 Agreements:
For NR, support both periodic and semi-persistent CSI reporting:
  For periodic: higher-layer configuration of reporting periodicity and timing offset
  FFS for the case of semi-persistent CSI reporting w.r.t. reporting periodicity and timing offset
  FFS on detailed signaling

## Slide 6
CSI reporting with two types of spatial information feedback is supported.
Type I feedback: Normal
  Type I feedback is codebook-based PMI feedback with normal spatial resolution
  Type I feedback supports at least the following (DL) CSI reporting parameters.
    Resource selection indicator (Examples for further study are reference signal resource, port, reference signal sequence, beam)
    RI (rank indicator)
    PMI (precoding matrix indicator)
    Channel quality feedback
Type II feedback: Enhanced
  “Explicit” feedback and/or codebook-based feedback with higher spatial resolution
For Type I and II, CSI feedback per subband as well as wideband feedback are supported. For Type I and II, beam-related feedback can be also included.

## Slide 7
With regard to relating CSI-RS transmission and CSI reporting, the following combinations are supported at least
  Aperiodic CSI reporting with aperiodic CSI-RS
  Aperiodic CSI reporting with semi-persistent/periodic CSI-RS
  Semi-persistent/periodic CSI reporting with semi-persistent/periodic CSI-RS
To support combinations above more flexibly, NR should allow independent control of CSI-RS indication and CSI reporting indication timings.
The indication may refer to triggering, activation, and deactivation depending on type of RS/reporting.

## Slide 8
CSI-related settings
  CSI reporting settings
  RS (at least for CSI measurement) settings, e.g. CSI-RS (CSI-IM as a special case)
  CSI measurement settings: To configure which RS setting is used for a particular CSI reporting setting

## Slide 9
DL DMRS based spatial multiplexing (SU-MIMO/MU-MIMO) is supported.
Dynamic switching between transmission methods/schemes is supported.
For coordinated transmission schemes for NR, both the case of co-located TRPs and the case of non-co-located TRPs are considered. For coordinated transmission schemes for NR, different types of coordinated transmission schemes for NR are supported.
Downlink transmission scheme(s) achieving diversity gain at least for some control information transmission is supported.

## Slide 10
#87 Agreements:
The number of codeword(s) per one scheduled physical data channel in NR both for DL and UL
  For 1-2 MIMO layers – FFS between 1 codeword and 2 codewords
  For 3-8 MIMO layers FFS among
    Alt 1: 1 codeword
    Alt 2: 2 codewords
    Alt 3: >= 3 codewords
  Study the above alternatives taking into account performance of NC-JT transmission from two or more beams/TRPs, overhead in DCI/UCI (ACK/NACK, CQI)
  Study support of overhead reduction schemes such indication for the maximum number of MIMO layers from TRP, ACK/NACK spatial bundling, etc.
  Study possible use of different modulations in single codeword
  Study the possibility of configurable number of codewords per UE by NW

## Slide 11
#87 Agreements:
Define at least two sets of transmission parameters, where
  Transmission parameter set 1: parameters configured (FFS: L1 or L2 or L3)
    For default transmission scheme, specify default values of parameters in the Transmission parameter set 1
      FFS: Whether default value can be derived implicitly
    Note that depending on parameter settings in transmission parameter set 1, the size of transmission parameter set 2, i.e. DCI size, may vary.
  Transmission parameter set 2: parameters indicated by physical layer (e.g. NR PDCCH channel)
    FFS whether multiple subsets is supported and how to simplify DCI format
  Note: some transmission parameter may belong to both set-1 and set-2
  Detail parameters and usage condition are TBD
NR-PDCCH
DCI

## Slide 12
At least 8 orthogonal DL DMRS ports are supported for SU-MIMO scheduling and at least 8 orthogonal DL DMRS ports are supported for MU-MIMO scheduling.

## Slide 13
#87 Agreements:
Support at least the following DMRS based DL MIMO transmissions for data in NR,
  Scheme 1: Closed-loop transmission where data and DMRS are transmitted with the same precoding matrix
    Demodulation of data at the UE does not require knowledge of the precoding matrix used at the transmitter
    Note: spatial multiplexing and rank-1 are included

## Slide 14
#87 Agreements:
  Scheme 2: Open loop and Semi-open loop transmissions where data and DMRS may or may not be restricted to be transmitted with the same precoding matrix
    Demodulation of data at the UE may or may not require knowledge of the relation between DMRS ports and data layers
    Note: DMRS can be precoded or not precoded
    Study the transmission schemes, e.g., SFBC, Large delay CDD, Layer shifting, small delay CDD
    Study the selection of transparent and/or non-transparent DMRS
      Transparent DMRS: DMRS and data precoded identically
      Non-transparent DMRS: DMRS and data precoded differently

## Slide 15
#87 Agreement:
Support variable/configurable DMRS pattern for data demodulation
  At least one configuration supports front-loaded DMRS pattern
  FFS: Time and/or frequency domain density can be configured
  FFS: RE location can be configured

## Slide 16
Interference measurement under different interference hypothesis should be supported in NR. For interference measurement, at least one of the following schemes is supported.
  Measurement subsets in both time and frequency domain
  Interference measurement restriction in both time and frequency domain

## Slide 17
Quasi-CoLocation (QCL)
Definition of quasi-colocation (QCL) is that two antenna ports are said to be quasi co-located if properties of the channel over which a symbol on one antenna port is conveyed can be inferred from the channel over which a symbol on the other antenna port is conveyed.
For DM-RS antenna ports, NR supports:
  All ports are quasi-collocated.
  Not all ports are quasi-collocated.

## Slide 18
#87 Agreements:
Study the need of supporting UE feedback and contents if needed to assist QCL association between reference signal resources/ports with respect to UE spatial QCL parameter(s) to support UE side beamforming/receiving procedure
Companies are encouraged to provide details of beamforming/receiving procedures and evaluate performance in terms of at least following metrics:
  RS overhead
  Overhead of UE feedback
  Spectral efficiency